Test result for GPRS modem (192.168.12.102)

* All the SIM’s used here are registered on the HOME network.

Attached are the log files:

Configuring Multitech Modem

- Model: MTCBA-G-EN-F1-EU Modem Bundle is installed and switched ON.

- The firmware is upgraded to 1.14 (mtcba-x-en-v114.zip) after the firmware upgrade the factory restore is done on modem

- The web browser is used to configure IP.

- PPP and DHCP server is disabled

- The SIM Card from carrier Hutch is installed

- Telnet to port 5000 is used to find the signal strength (AT+CSQ  ) value=11

- Telnet to the port 5000 is very erratic using telnet xp client (screen shot- connection to host lost).

- The modem is inaccessible using raw protocol on Putty (screen shot – putty)

- Some observations

a) Telnet to modem is very erratic. 
b) Disconnect command “+++ ATH” to quit from the system is not functional.

Configuring Modem with Now SMS

1.NowSms is  installed and upgraded to latest version(patch2006.EXE)

2.The following smsgw.INI file is created manually

[SMSGW]

Debug=Yes

Modem1=IPModem - 192.168.12.102:5000

WebAuth=No

WebMenu=Yes

WebPort=8800

ReceiveSMS=Yes

ReceiveMMS=No

ReceiveSMSCharset=utf-8

ReceiveSMSCommand1=*	c:\windows\system32\cmd.exe /c echo Echo @@FULLSMS@@	No

SMPPPort=5000

IPAddress=192.168.12.108

[IPModem - 192.168.12.102:5000]

Username=*****

Password=*****

ReceiveSMS=Yes

ReceiveTo=Direct

ReceiveMMS=No

Observations

1) Delay in sending messages

2) After a Long Idle period modem does not respond or send SMS unless hard reboot

is done.

SMSOUT log shows the following error

“2007-01-08 12:45:44, System,, IPModem - 192.168.12.102:5000,Modem Failure -- Unable to access modem, ensure that it is powered on and passes diagnostic tests.”

3) Some of the messages are duplicated while sending as well as receiving.

4) Attached is the NowSMS setup as configured.