# Sony Ericsson T610

## Configuration instruction for WAP/GPRS

### Follow these instructions starting from the idle screen display of the handset

- Press the joystick button. Scroll to “Connectivity” (bottom left icon) and press “Select”

- Scroll down to “WAP options” (4th option) then press “Select” to enter the “WAP options” menu

- Press “Select” again to enter the “WAP profile” menu

- Press “Add” to add a new profile

- Enter GeeWAP as the new profile name and press “Ok”

- At the “Connect using:” option, press “Edit”

- Press “Add” to add a new data account

- Scroll down to “GSM data” and press “Select”

- Enter GeeWAP as the new data account name and press “Ok”

- Press “Edit” to enter the dial-up phone number

- Enter 98540070 and press “Ok”

- Scroll down to “User id” and press “Edit”.

- Enter star and press “Ok”

- Scroll down to “Password” and press “Edit”

- Enter hub and press “Ok”

- Press “Save” to save settings. A message “New GSM data account created” will be displayed.

- Scroll to “GeeWAP” and press “Select”

- Scroll down to “IP address” and press “Edit”

- Enter 010.012.001.002 and press “Ok”

- Press “Save” to save settings. A message “New profile created” will be displayed.

- Scroll to “GeeWAP” and press “Edit”

- Scroll down to “Advanced” (4th option) and press “Select”

- Press “Select” again to change the homepage settings

- Delete the text “internet service”. Enter GeeWAP as the homepage name and press “Ok”

- Delete the text “Internal address”

- Enter http://gee-select.starhubgee.com.sg/wap/ and press “Ok”

- Press the Return button twice (the button with a U-turn arrow symbol) to return to the WAP profiles menu

- Scroll up to “New profile” and press “Add”

- Enter GeeGPRS and press “Ok”

- At the “Connect using:” option, press “Edit”

- Scroll up to “New account” and press “Add”

- Scroll up to “GPRS data” and press Select”

- Enter GeeGPRS as the new data account name and press “Ok”

- Press “Edit” to edit “APN”

- Enter shwap and press “Ok”

- Leave the “User id” and “Password” options blank.

- Press “Save” to save settings. A message “New GPRS data account created” will be displayed.

- Scroll down to “GeeGPRS” and press “Select”

- Scroll down to “IP address” and press “Edit”

- Enter 010.012.001.002 and press “Ok”

- Press “Save”. A message “New Profile created” will be displayed

- Scroll up to “ GeeGPRS” in the “WAP profile” menu and press “Edit”

- Scroll down to “Advanced” and press “Select”

- Press “Select” again to change homepage settings

- Delete the text “internet service”. Enter GeeGPRS as the homepage name and press “Ok”

- Delete the text “Internal address”.

- Enter http://gee-select.starhubgee.com.sg/wap/ and press “Ok”

- Press the Return button twice to return to the “WAP profile” menu

- Scroll up to “GeeGPRS” and press “Select”

- Press the Return button twice to return to the main menu. Phone is now configured for WAP over GPRS.

## Configuration instruction for MMS

Start these instructions from the idle screen of the handset.

- Press the joystick button. Scroll to “Messaging” and press “Select”

- Scroll down to “Picture” (2nd option) and press “Select”

- Scroll down to “Options” and press “Select”

- Scroll down to “Message server” (6th option) and press “Select”

- Enter http://mms.starhubgee.com.sg:8002 and press “Ok”

- Scroll down to “WAP profile” and press “Select”

- Scroll down to “Create new” and press “Select”

- Enter GeeMMS as the new profile name and press “Ok”

- At the “Connect using:” option, press “Edit”

- Scroll up to “New account” and press “Add” to create a new data account

- Scroll to “GPRS data” and press “Select”

- Enter GeeMMS and press “Ok”

- Press “Edit” to edit “APN”

- Enter shmms and press “Ok”

- Leave the “User id” and the “Password” options blank

- Press “Save” to save settings. A message “New GPRS data account created” will be displayed

- Scroll down to “GeeMMS” and press “Select”

- Scroll down to “IP address” and press “Edit”

- Enter 010.012.001.080 and press “Ok”

- Press “Save” to save settings. A message “New profile created” will be displayed

- Scroll up to “ Select” at the “WAP profile” menu and press “Select”

- Scroll to “GeeMMS” and press “Select” to use the GeeMMS as the default profile used for MMS.

- Press Return button 4 times to return to the main menu. Handset is now ready to send MMS.